## Slide 1: Computer Networks
Stobak Dutta
Dept of CST
UEM, Kolkata

## Slide 2: Switching
This technique of transferring the information from one computer network to another network is known as switching.
Switching in a computer network is achieved by using switches. A switch is a small hardware device which is used to join multiple computers together with one local area network (LAN).
Network switches operate at layer 2 (Data link layer) in the OSI model.
Switching is transparent to the user and does not require any configuration in the home network.
Switches are used to forward the packets based on MAC addresses.
A Switch is used to transfer the data only to the device that has been addressed. It verifies the destination address to route the packet appropriately.

## Slide 3: Switching Modes
There are three types of switching modes:
Store-and-forward
  The layer 2 switch waits until the entire frame has received. On receiving the entire frame, switch store the frame into the switch buffer memory. This process is known as storing the frame.
  When the frame is stored, then the frame is checked for the errors. If any error found, the message is discarded otherwise the message is forwarded to the next node. This process is known as forwarding the frame.

## Slide 4
Cut-through
  Cut-through switching is a technique in which the switch forwards the packets after the destination address has been identified without waiting for the entire frame to be received.
  Once the frame is received, it checks the first six bytes of the frame following the preamble, the switch checks the destination in the switching table to determine the outgoing interface port, and forwards the frame to the destination.

## Slide 5
Fragment-free
  A Fragment-free switching is an advanced technique of the Cut-through Switching.
  A Fragment-free switching is a technique that reads atleast 64 bytes of a frame before forwarding to the next node to provide the error-free transmission.
  It combines the speed of Cut-through Switching with the error checking functionality.

## Slide 6: Switching techniques
Circuit Switching
  Circuit switching is a switching technique that establishes a dedicated path between sender and receiver.
  In the Circuit Switching Technique, once the connection is established then the dedicated path will remain to exist until the connection is terminated.
Message Switching
  Message Switching is a switching technique in which a message is transferred as a complete unit and routed through intermediate nodes at which it is stored and forwarded.
  In Message Switching technique, there is no establishment of a dedicated path between the sender and receiver.
  The destination address is appended to the message. Message Switching provides a dynamic routing as the message is routed through the intermediate nodes based on the information available in the message.

## Slide 7
Packet Switching
  The packet switching is a switching technique in which the message is sent in one go, but it is divided into smaller pieces, and they are sent individually.
  The message splits into smaller pieces known as packets and packets are given a unique number to identify their order at the receiving end.
  Every packet contains some information in its headers such as source address, destination address and sequence number.
  Packets will travel across the network, taking the shortest path as possible.
  All the packets are reassembled at the receiving end in correct order.
  If any packet is missing or corrupted, then the message will be sent to resend the message.
  If the correct order of the packets is reached, then the acknowledgment message will be sent.

## Slide 8
Network Layer
The Network Layer is the third layer of the OSI model.
It handles the service requests from the transport layer and further forwards the service request to the data link layer.
The network layer translates the logical addresses into physical addresses
It determines the route from the source to the destination and also manages the traffic problems such as switching, routing and controls the congestion of data packets.
The main role of the network layer is to move the packets from sending host to the receiving host.

## Slide 10: Class A
The network ID is 8 bits long.
The host ID is 24 bits long.
In Class A, the first bit in higher order bits of the first octet is always set to 0 and the remaining 7 bits determine the network ID. The 24 bits determine the host ID in any network.
The total number of networks in Class A = 27 = 128 network address
The total number of hosts in Class A = 224 - 2 = 16,777,214 host address

## Slide 11: Class B
In Class B, an IP address is assigned to those networks that range from small-sized to large-sized networks.
The Network ID is 16 bits long.
The Host ID is 16 bits long.
In Class B, the higher order bits of the first octet is always set to 10, and the remaining14 bits determine the network ID. The other 16 bits determine the Host ID.
The total number of networks in Class B = 214 = 16384 network address
The total number of hosts in Class B = 216 - 2 = 65534 host address

## Slide 12
In Class C, an IP address is assigned to only small-sized networks.
The Network ID is 24 bits long.
The host ID is 8 bits long.
In Class C, the higher order bits of the first octet is always set to 110, and the remaining 21 bits determine the network ID. The 8 bits of the host ID determine the host in a network.
The total number of networks = 221 = 2097152 network address
The total number of hosts = 28 - 2 = 254 host address

## Slide 13
Rules for assigning Host ID:
The Host ID is used to determine the host within any network. The Host ID is assigned based on the following rules:
The Host ID must be unique within any network.
The Host ID in which all the bits are set to 0 cannot be assigned as it is used to represent the network ID of the IP address.
The Host ID in which all the bits are set to 1 cannot be assigned as it is reserved for the multicast address.

## Slide 14
Rules for assigning Network ID:
If the hosts are located within the same local network, then they are assigned with the same network ID. The following are the rules for assigning Network ID:
The network ID cannot start with 127
The Network ID in which all the bits are set to 0 cannot be assigned as it is used to specify a particular host on the local network.
The Network ID in which all the bits are set to 1 cannot be assigned as it is reserved for the multicast address.

## Slide 15: Routing
Routing is a process of selecting path along which the data can be transferred from source to the destination. Routing is performed by a special device known as a router.
A Router works at the network layer in the OSI model and internet layer in TCP/IP model
A router is a networking device that forwards the packet based on the information available in the packet header and forwarding table.
The routing algorithms are used for routing the packets. The routing algorithm is nothing but a software responsible for deciding the optimal path through which packet can be transmitted.
The routing protocols use the metric to determine the best path for the packet delivery. The metric is the standard of measurement such as hop count, bandwidth, delay, current load on the path, etc. used by the routing algorithm to determine the optimal path to the destination.
The routing algorithm initializes and maintains the routing table for the process of path determination.

## Slide 16: Routing Metrics and Costs
Routing metrics and costs are used for determining the best route to the destination. The factors used by the protocols to determine the shortest path are known as a metric.
Metrics are the network variables used to determine the best route to the destination. Some protocols use the static metrics means that their value cannot be changed and for some other routing protocols use the dynamic metrics means that their value can be assigned by the system administrator.

## Slide 17
The most common metric values are :
Hop count: Hop count is defined as a metric that specifies the number of passes through internetworking devices such as a router, a packet must travel in a route to move from source to the destination. If the routing protocol considers the hop as a primary metric value, then the path with the least hop count will be considered as the best path to move from source to the destination.
Delay: It is a time taken by the router to process, queue and transmit a datagram to an interface. The protocols use this metric to determine the delay values for all the links along the path end-to-end. The path having the lowest delay value will be considered as the best path.
Bandwidth: The capacity of the link is known as a bandwidth of the link. The bandwidth is measured in terms of bits per second. The link that has a higher transfer rate like gigabit is preferred over the link that has the lower capacity like 56 kb. The protocol will determine the bandwidth capacity for all the links along the path, and the overall higher bandwidth will be considered as the best route.

## Slide 18
Load: Load refers to the degree to which the network resource such as a router or network link is busy. A Load can be calculated in a variety of ways such as CPU utilization, packets processed per second. If the traffic increases, then the load value will also be increased. The load value changes with respect to the change in the traffic.
Reliability: Reliability is a metric factor may be composed of a fixed value. It depends on the network links, and its value is measured dynamically. Some networks go down more often than others. After network failure, some network links repaired more easily than other network links. Any reliability factor can be considered for the assignment of reliability ratings, which are generally numeric values assigned by the system administrator.

## Slide 19: Types of Routing
Static Routing
Default Routing
Dynamic Routing

## Slide 20: Static Routing
Static Routing is also known as Nonadaptive Routing.
It is a technique in which the administrator manually adds the routes in a routing table.
A Router can send the packets for the destination along the route defined by the administrator.
In this technique, routing decisions are not made based on the condition or topology of the networks
Advantages Of Static Routing
No Overhead: It has no overhead on the CPU usage of the router. Therefore, the cheaper router can be used to obtain static routing.
Bandwidth: It has less bandwidth usage between the routers.
Security: It provides security as the system administrator is allowed only to have control over the routing to a particular network.
Disadvantages of Static Routing:
For a large network, it becomes a very difficult task to add each route manually to the routing table.
The system administrator should have a good knowledge of a topology as he has to add each route manually.

## Slide 21: Default Routing
Default Routing is a technique in which a router is configured to send all the packets to the same hop device, and it doesn't matter whether it belongs to a particular network or not. A Packet is transmitted to the device for which it is configured in default routing.
Default Routing is used when networks deal with the single exit point.
It is also useful when the bulk of transmission networks have to transmit the data to the same hop device.
When a specific route is mentioned in the routing table, the router will choose the specific route rather than the default route. The default route is chosen only when a specific route is not mentioned in the routing table.

## Slide 22: Dynamic Routing
It is also known as Adaptive Routing.
It is a technique in which a router adds a new route in the routing table for each packet in response to the changes in the condition or topology of the network.
Dynamic protocols are used to discover the new routes to reach the destination.
In Dynamic Routing, RIP and OSPF are the protocols used to discover the new routes.
If any route goes down, then the automatic adjustment will be made to reach the destination.
The Dynamic protocol should have the following features:
All the routers must have the same dynamic routing protocol in order to exchange the routes.
If the router discovers any change in the condition or topology, then router broadcast this information to all other routers.

## Slide 23
Advantages of Dynamic Routing:
It is easier to configure.
It is more effective in selecting the best route in response to the changes in the condition or topology.
Disadvantages of Dynamic Routing:
It is more expensive in terms of CPU and bandwidth usage.
It is less secure as compared to default and static routing.

## Slide 24: ARP
ARP stands for Address Resolution Protocol.
It is used to associate an IP address with the MAC address.
Each device on the network is recognized by the MAC address imprinted on the NIC. Therefore, we can say that devices need the MAC address for communication on a local area network. MAC address can be changed easily. For example, if the NIC on a particular machine fails, the MAC address changes but IP address does not change. ARP is used to find the MAC address of the node when an internet address is known.

## Slide 25
There are two types of ARP entries:
Dynamic entry: It is an entry which is created automatically when the sender broadcast its message to the entire network. Dynamic entries are not permanent, and they are removed periodically.
Static entry: It is an entry where someone manually enters the IP to MAC address association by using the ARP command utility.

## Slide 26: RARP
RARP stands for Reverse Address Resolution Protocol.
If the host wants to know its IP address, then it broadcast the RARP query packet that contains its physical address to the entire network. A RARP server on the network recognizes the RARP packet and responds back with the host IP address.
The protocol which is used to obtain the IP address from a server is known as Reverse Address Resolution Protocol.
The message format of the RARP protocol is similar to the ARP protocol.
Like ARP frame, RARP frame is sent from one machine to another encapsulated in the data portion of a frame

## Slide 27: ICMP
ICMP stands for Internet Control Message Protocol.
The ICMP is a network layer protocol used by hosts and routers to send the notifications of IP datagram problems back to the sender.
ICMP uses echo test/reply to check whether the destination is reachable and responding.
ICMP handles both control and error messages, but its main function is to report the error but not to correct them.
An IP datagram contains the addresses of both source and destination, but it does not know the address of the previous router through which it has been passed. Due to this reason, ICMP can only send the messages to the source, but not to the immediate routers.
ICMP protocol communicates the error messages to the sender. ICMP messages cause the errors to be returned back to the user processes.
ICMP messages are transmitted within IP datagram.

## Slide 28
ICMP protocol reports the error messages to the sender.
Five types of errors are handled by the ICMP protocol:
Destination unreachable
Source Quench
Time Exceeded
Parameter problems
Redirection

## Slide 29
Destination unreachable: The message of "Destination Unreachable" is sent from receiver to the sender when destination cannot be reached, or packet is discarded when the destination is not reachable.
Source Quench: The purpose of the source quench message is congestion control. The message sent from the congested router to the source host to reduce the transmission rate. ICMP will take the IP of the discarded packet and then add the source quench message to the IP datagram to inform the source host to reduce its transmission rate. The source host will reduce the transmission rate so that the router will be free from congestion.
Time Exceeded: Time Exceeded is also known as "Time-To-Live". It is a parameter that defines how long a packet should live before it would be discarded.
There are two ways when Time Exceeded message can be generated:
Sometimes packet discarded due to some bad routing implementation, and this causes the looping issue and network congestion. Due to the looping issue, the value of TTL keeps on decrementing, and when it reaches zero, the router discards the datagram. However, when the datagram is discarded by the router, the time exceeded message will be sent by the router to the source host.
When destination host does not receive all the fragments in a certain time limit, then the received fragments are also discarded, and the destination host sends time Exceeded message to the source host.
Parameter problems: When a router or host discovers any missing value in the IP datagram, the router discards the datagram, and the "parameter problem" message is sent back to the source host.
Redirection: Redirection message is generated when host consists of a small routing table. When the host consists of a limited number of entries due to which it sends the datagram to a wrong router. The router that receives a datagram will forward a datagram to a correct router and also sends the "Redirection message" to the host to update its routing table.

## Slide 30: IGMP
IGMP stands for Internet Group Message Protocol.
The IP protocol supports two types of communication:
  Unicasting: It is a communication between one sender and one receiver. Therefore, we can say that it is one-to-one communication.
  Multicasting: Sometimes the sender wants to send the same message to a large number of receivers simultaneously. This process is known as multicasting which has one-to-many communication.
The IGMP protocol is used by the hosts and router to support multicasting.
The IGMP protocol is used by the hosts and router to identify the hosts in a LAN that are the members of a group.

## Slide 31: Routing algorithm
In order to transfer the packets from source to the destination, the network layer must determine the best route through which packets can be transmitted.
Whether the network layer provides datagram service or virtual circuit service, the main job of the network layer is to provide the best route. The routing protocol provides this job.
The routing protocol is a routing algorithm that provides the best path from the source to the destination. The best path is the path that has the "least-cost path" from source to the destination.
Routing is the process of forwarding the packets from source to the destination but the best route to send the packets is determined by the routing algorithm.
Classification of a Routing algorithm
The Routing algorithm is divided into two categories:
Adaptive Routing algorithm
Non-adaptive Routing algorithm

## Slide 32: Adaptive Routing algorithm
An adaptive routing algorithm is also known as dynamic routing algorithm.
This algorithm makes the routing decisions based on the topology and network traffic.
The main parameters related to this algorithm are hop count, distance and estimated transit time.
An adaptive routing algorithm can be classified into three parts:
Centralized algorithm: It is also known as global routing algorithm as it computes the least-cost path between source and destination by using complete and global knowledge about the network. This algorithm takes the connectivity between the nodes and link cost as input, and this information is obtained before actually performing any calculation. Link state algorithm is referred to as a centralized algorithm since it is aware of the cost of each link in the network.
Isolation algorithm: It is an algorithm that obtains the routing information by using local information rather than gathering information from other nodes.
Distributed algorithm: It is also known as decentralized algorithm as it computes the least-cost path between source and destination in an iterative and distributed manner. In the decentralized algorithm, no node has the knowledge about the cost of all the network links. In the beginning, a node contains the information only about its own directly attached links and through an iterative process of calculation computes the least-cost path to the destination. A Distance vector algorithm is a decentralized algorithm as it never knows the complete path from source to the destination, instead it knows the direction through which the packet is to be forwarded along with the least cost path.

## Slide 33: Non-Adaptive Routing algorithm
Non Adaptive routing algorithm is also known as a static routing algorithm.
When booting up the network, the routing information stores to the routers.
Non Adaptive routing algorithms do not take the routing decision based on the network topology or network traffic.
The Non-Adaptive Routing algorithm is of two types:
Flooding: In case of flooding, every incoming packet is sent to all the outgoing links except the one from it has been reached. The disadvantage of flooding is that node may contain several copies of a particular packet.
Random walks: In case of random walks, a packet sent by the node to one of its neighbors randomly. An advantage of using random walks is that it uses the alternative routes very efficiently.

## Slide 34: Distance Vector Routing Algorithm
The Distance vector algorithm is iterative, asynchronous and distributed.
  Distributed: It is distributed in that each node receives information from one or more of its directly attached neighbors, performs calculation and then distributes the result back to its neighbors.
  Iterative: It is iterative in that its process continues until no more information is available to be exchanged between neighbors.
  Asynchronous: It does not require that all of its nodes operate in the lock step with each other.
The Distance vector algorithm is a dynamic algorithm.
It is mainly used in ARPANET, and RIP.
Each router maintains a distance table known as Vector.
Three Keys to understand the working of Distance Vector Routing Algorithm:
Knowledge about the whole network: Each router shares its knowledge through the entire network. The Router sends its collected knowledge about the network to its neighbors.
Routing only to neighbors: The router sends its knowledge about the network to only those routers which have direct links. The router sends whatever it has about the network through the ports. The information is received by the router and uses the information to update its own routing table.
Information sharing at regular intervals: Within 30 seconds, the router sends the information to the neighboring routers.

## Slide 35: Link State Routing
Link state routing is a technique in which each router shares the knowledge of its neighborhood with every other router in the internetwork.
The three keys to understand the Link State Routing algorithm:
Knowledge about the neighborhood: Instead of sending its routing table, a router sends the information about its neighborhood only. A router broadcast its identities and cost of the directly attached links to other routers.
Flooding: Each router sends the information to every other router on the internetwork except its neighbors. This process is known as Flooding. Every router that receives the packet sends the copies to all its neighbors. Finally, each and every router receives a copy of the same information.
Information sharing: A router sends the information to every other router only when the change occurs in the information.
Link State Routing has two phases:
Reliable Flooding
Initial state: Each node knows the cost of its neighbors.
Final state: Each node knows the entire graph.
Route Calculation
Each node uses Dijkstra's algorithm on the graph to calculate the optimal routes to all nodes.
The Link state routing algorithm is also known as Dijkstra's algorithm which is used to find the shortest path from one node to every other node in the network.
The Dijkstra's algorithm is an iterative, and it has the property that after kth iteration of the algorithm, the least cost paths are well known for k destination nodes.